## Slide 1
Amin Sarihi
Hardware Trojan Insertion and Detection Using Reinforcement Learning
Ph.D. Candidate at
Klipsch School of ECE, New Mexico State University
Notes: Good Morning. I would like to thank the committee members for taking the time to review my report and being here to participate in this session.

## Slide 2: Outlines
1
Introduction
Problem Statement
Reinforcement Learning
Hardware Trojan Insertion
Hardware Trojan Detection
Adversarial HT Insertion
Real-world HT Benchmarking
Conclusion

## Slide 3
1
Introduction

## Slide 4: Introduction
Hardware designs had long been deemed secure
Side-channel attacks in late 90’s [1]
Hardware Trojan (HT) coined in 2007 [2]
  Malicious hardware modifications
  Lead to secret leakage or chip malfunction
Chips are widely used in various civilian and military applications
[1] Paul Kocher, Joshua Jaffe, and Benjamin Jun. Differential power analysis. In Advances in Cryptology—CRYPTO’99: 19th Annual International Cryptology Conference Santa Barbara, California, USA, August 15–19, 1999 Proceedings 19, pages 388–397. Springer, 1999.
[2] Dakshi Agrawal, Selcuk Baktir, Deniz Karakoyunlu, Pankaj Rohatgi, and Berk Sunar. Trojan detection using ic fingerprinting. In 2007 IEEE Symposium on Security and Privacy (SP’07), pages 296–310. IEEE, 2007
Notes: So, it is very important to have proper security mechanisms to counter the threats on chips.

## Slide 5: Introduction
1
1
Trigger
Payload
A
B
C
D
A=1
B=1
C=0
D=1
E is flipped!
An HT Example
1
1
1
1
0
1
Rare
Nets
Circuit Nets
Towards
Output
c7552 has 207 inputs , i.e., 2207 input patterns, larger than the estimated number of atoms in the universe!
Discovering HTs are not easy!
Notes: The Trojan circuits consists of two parts: Trigger and Payload
From attacker’s POV, the HT should not be activated frequently. If activated frequently, the existence of the HT will be given away.

## Slide 6
1
Problem Statement

## Slide 7
Problem Statement
Silicon Supply Chain Stages
Specification
RTL Design/
Behavioral Level
Netlist / Gate Level
Physical Design Layout
Fabrication
Assembly & Testing
Market
IP Core
EDA Tools
Functionality
Performance Req
Architecture
3PIP
Reverse-engineering

## Slide 8: Problem Statement
To study HTs, we need HT Benchmarks. The most referenced HT benchmark is from trust-hub.org:
Limited Dataset on trust-hub.org
  The number of HT-infected circuits is very limited
  HT insertion is done through a one-dimensional lens
  Fine-tuned HT detectors
Lack of circuit variety
  Impossible to insert HTs in different circuits
Reinforcement Learning emerges as a viable solution!

## Slide 9
1
Reinforcement Learning

## Slide 10: Background Theory
Reinforcement Learning
A
B
Action at
Reward rt+1
State st+1
Reward r
State st
Agent
Environment
The agent’s goal is to maximize the sum of collected rewards over all episodes
Notes: 1- Reinforcement Learning is a machine learning strategy for decision-making through trial and error

## Slide 11
1
HT Insertion

## Slide 12: HT Insertion
Flow of the Insertion Tool
SCOAP (Sandia Controllability/Observability Analysis Program) Measures
Controllability: a measure for the difficulty of setting a particular net in a design to either ’0’ or ’1’.
Observability: a measure for the difficulty of propagating a net value to at least one of the circuit’s primary outputs
Notes: We must specify the trigger nets or the rare nets.

## Slide 13: HT Insertion
0
0
0
0
0
0
1
2
1
3
2
3
4
S1
S2
S3
S4
…
Payload
Logic
Trigger
Logic
Target net
Trigger
Nets
HT Insertion with RL
Next Level
Previous Level
Same Level Up
Same Level Down
No Action
|
|
|
|
|
|
|
|
|
|
|
|
|
|
|
State space: logic-levels of the HT connections
Action space
Action space: Encoding actions 0-4

## Slide 14: HT Insertion
The HT Insertion Algorithm & Rewarding
Insert the HT randomly in the circuit
HT trigger nets start moving (actions are taken)
HT functionality is tested with PODEM
  Functional Agent is rewarded + based on the number of rare triggers
  Not functional or no rare triggers Agent is rewarded -1
Agent resets when terminal state is reached

## Slide 15
1
HT Detection

## Slide 16: HT Detection
Flow of the Detection Tool
Generate test vectors that activate rare nets many times!
The detection agent’s goal is to activate as many rare nets as it can
Dynamic Sim: Record Switching activities with 100k random test vectors
Static Sim: Derive the HTS values for each net
Notes: In summary, the goal of the HT detector is to generate test vectors that activate the identified rare nets as much as possible.

## Slide 17: HT Detection
Action Space
number of circuit inputs
Binary actions:
  0. Leave it unchanged 1. Flip the bit
Old Test Vector
Action
⊕
New Test Vector
State Space
number of rare nets
State Space
Action
Rare Nets Status
New State

## Slide 18: HT Detection
Detection Rewarding Function D1
Test vectors are generated (actions are taken)
Count the number of activated rare nets
Keep a copy of the previous state
Net-wise comparison of the new and previous states
  The most + reward an inactive net becomes active
  The most - reward an active net becomes inactive

## Slide 19: HT Detection
Detection Rewarding Function D2
Target nets are based on switching activities
Rare nets’ switching vector is passed to the algorithm
Test patterns are generated (actions are taken)
Rewards are proportionate to the inverse of switching activities
The more the rare nets are activated The higher the reward

## Slide 20: HT Detection
Detection Rewarding Function D3
Target nets are based on controllability
Nets’ controllability vector is passed to the algorithm
Test patterns are generated (actions are taken)
Rewards are proportionate to the controllability amounts
The more the rare nets are activated The higher the reward

## Slide 21: Results and Analysis
HT Detection Figures for D1, D2, D3 Detectors [1]
Payload is placed Randomly
The combined detector includes D1, D2, and D3
[1] Sarihi, A., Patooghy, A., Jamieson, P. and Badawy, A.H.A., 2024. Trojan playground: a reinforcement learning framework for hardware Trojan insertion and detection. The Journal of Supercomputing, pp.1-35.
Notes: We collected the first 20k test vectors with a reward threshold of 1/10 of the reward in the last episode
Despite more inserted HTs in the 𝑷_𝒉𝒊𝒈𝒉 scenario, they do not evade detection any better than 𝑷_𝒓𝒂𝒏𝒅 BUT they can be used to train better ML HT detectors.
The impact of the Combined scenario is significant, e.g., in c3540, none of D1, D2, and D3 perform better than 60%, while Combined reaches 75%.
Another important observation can be made for c2670
  D1 achieves 10% detection accuracy
  D3 achieves nearly 90% detection accuracy
More test vectors yield significantly higher accuracy, e.g., in c3540, we collected 191K , 183K , 121K for D1, D2, and D3 and the detection rates were 89%, 86%, and 97%, respectively
While accuracy is 100% in c6288, the same figure is about 25%-30% lower in c3540 and c7552
  c6288 is a multiplier circuit with no control signals
  c3540, on the other hand, has 14 control inputs for multiplexing and masking data
  Similar case for c7552 with multiple controls signals
  Our hypothesis is that inserting HTs in control paths can lead to stealthier HTs than data paths in circuits.
Detection accuracy is lower in c432 while it is smaller
  The rarest net was triggered only 7%, other circuits have nets with switching activities well below 1%
  20K random test patterns detected 99% of HTs

## Slide 22: Results and Analysis
RL Agents Performance
The insertion agent in c5315 [1]
The insertion agent in c5315 [1]
[1] Sarihi, A., Patooghy, A., Jamieson, P. and Badawy, A.H.A., 2024. Trojan playground: a reinforcement learning framework for hardware Trojan insertion and detection. The Journal of Supercomputing, pp.1-35.
Notes: In the insertion phase, the agent tends to finish the episodes in the beginning to avoid further losses
After several thousand timesteps, it learns how to accumulate positive rewards and increase the episode length
In the detection phase, the agent collects positive rewards along the way; however, it hits diminishing returns
The trade-off between training time and detection accuracy must be considered

## Slide 23: Results and Analysis
RL Agents Performance (Contd.)
The detection agent in c5315
[1] Sarihi, A., Patooghy, A., Jamieson, P. and Badawy, A.H.A., 2024. Trojan playground: a reinforcement learning framework for hardware Trojan insertion and detection. The Journal of Supercomputing, pp.1-35.
Notes: In the detection phase, the agent collects positive rewards along the way; however, it hits diminishing returns
The trade-off between training time and detection accuracy must be considered

## Slide 24: Results and Analysis
Our Detection Accuracy vs. Two state-of-the-art Detectors [1]
24
[1] Sarihi, A., Patooghy, A., Jamieson, P. and Badawy, A.H.A., 2024. Trojan playground: a reinforcement learning framework for hardware Trojan insertion and detection. The Journal of Supercomputing, pp.1-35.
Notes: Combined vs DETERRENT
Combined outperforms DETERRENT in all 4 circuits.
The detection gap is significant in c2670 and c5315
Our tool insertion criteria is not fully captured in DETERRENT’s detection capabilities
________________________________________________________________________________________________________________________________________
Combined vs HW2VEC
Scenario I:
Train data: TJ_RTL, Test data: Our inserted HTs + two versions of ISCAS-85 HT-free benchmarks
HW2VEC shows a detection rate of 87% across all 4 circuits with 0 FPs
Scenario II:
Train: TJ_RTL + EPFL [1], Test: Similar to the previous scenario
HW2VEC detection rate drops to 48% with 0 FPs
ML HT detectors are very sensitive to the train data
More HT benchmarks are needed for better training
Combined still performs better than DETERRENT in 3 cases

## Slide 25
1
Adversarial HT Insertion

## Slide 26: Detection-Insertion Loop
Agent
Detect Trojans
Hide Trojans
  Create a loop that combines an HT inserting agent with an HT detector
  The goal is to create HT instances that outsmart the current detectors
Adversarial HT Insertion Flow

## Slide 27: Functional and Structural Pruning
Structural Pruning
Functional Pruning
After both pruning methods take place, we select 20 random trigger nets to build HT instances.

## Slide 28: Attack Success Rates
[2] Sarihi, A., Jamieson, P., Patooghy, A., and Badawy, A. A., 2024, September. TrojanForge: Generating Adversarial Hardware Trojan Examples Using Reinforcement Learning, In Proceedings of the 2024 ACM/IEEE Workshop on Machine Learning for CAD.

## Slide 29
1
Real-world HT Benchmarking

## Slide 30: Real-world Benchmarking
Comparison of a) current HT detection approaches with static HT benchmarks that only contain HT-infected circuits vs. b) our proposed HT detection flow, including restructured benchmarks with and without HTs
Most HT detectors are trained on trust-hub.org benchmark suffering many issues:
Only three out of 83 studied HT circuits are usable in real-world scenarios
The major issues were pre-synthesis and post-synthesis discrepancies, unsatisfiable trigger conditions, and incorrect original designs [3].
Krieg, C., 2023, October. Reflections on trusting TrustHUB. In 2023 IEEE/ACM International Conference on Computer Aided Design (ICCAD) (pp. 1-9). IEEE.
30

## Slide 31: Graph Structural Analysis
One of the recent HT detection ideas: HW2VEC HT detector:
Uses GNNs (Graph Neural Networks) for HT detection
Extracts graph representations from hardware designs
HW2VEC provides 200 data points for each circuit
Question: Does graph restructuring techniques change the circuit representation?
For more circuit variety, we can use ABC, an open-source logic optimization tool to transform each circuit graph to its equivalent AND-inverter-graph (AIG) circuit representation
31

## Slide 32: PCA Analysis Findings
PCA analysis of hidden HTs vs. clean functionally transformed ISCAS-85 circuits
HT-free and HT-infected circuits have very similar distributions after functional restructuring!
32
Before graph restructuring
After graph restructuring (AIG)

## Slide 33
Impact of training dataset on HT Detection
The HT detection accuracy spans between 0%
and 80% for S1
The HT detection accuracy spans between 0%
and 20% for S2
S1: 26 HT-infected and 11 HT-free instances. S2: 26 HT-infected and 27 HT-free instances.
The training data heavily impacts the HT detection accuracy!
HT detection accuracy of 18 functionally equivalent transformation methods trained with a) S1 and b) S2 for ISCAS-85 benchmarks.
33

## Slide 34
1
Conclusion & Future Work

## Slide 35: Conclusion & Future Work
1
Conclusion:
  Introduced automated multi-criteria HT insertion and detection
  Demonstrated the vulnerabilities of HT detectors by generating adversarial HT instances in a GAN-like loop
  Introduced a new HT benchmarking approach to mimic HT detection in a real-world scenario
Future directions:
  Add support for sequential circuits
  Experiment with circuit restructuring techniques in a GAN-like loop

## Slide 36
1
Thank You!